## Slide 1
PROOFSHAPE
Smartphone 3D Inspection Checkpoint Review
Mobile capture → metric reconstruction → provenance-aware inspection
13-WEEK CAPSTONE
3-PERSON TEAM
OCT 29, 2026
Current checkpoint
Phone capture is connected to the real service. Metric alignment, confidence-gated provenance, uncertainty, and AI frame supervision are working. CAD registration is the next inspection milestone.
PROOFSHAPE • CHECKPOINT • 1/10

## Slide 2
TEAM
Three contributors, one inspection pipeline
Mamadou Jallow · @mbj1994
Reconstruction & integration • Provenance / uncertainty • Metric alignment support • VLM supervision • CAD loading + I-03 registration
Yashi Dalwala · @dalwalyk
Capture & inspection • Capture → service integration • CAD / OBJ loading • Device validation • Cross-machine testing
Tabeen Raoof · @TabeenRaoof
Reconstruction validation • Golden-set reruns • Metric / board validation • Review & clean checkout • Measurement evidence
PROOFSHAPE • CHECKPOINT • 2/10

## Slide 3
PROGRESS 1/4
Phone capture now reaches the real reconstruction service
C-13 closed the gap between the browser capture flow and recon.service.
REAL-PHONE EVIDENCE
iPhone → HTTPS dev proxy → recon.service
14-frame clean-checkout session completed on M3 Pro
metric: true • ChArUco reference tier
observed_fraction: 0.1395
638 KB GLB produced on disk
What changed
EXIF-less phone frames are calibrated from the printed ChArUco board; the same-origin proxy lets the phone reach the real service without a second certificate.
What we learned
The end-to-end path works, but phone reliability is not solved yet: early tests exposed board-calibration and fusion failure modes. Failures now report their real cause instead of failing silently.
PROOFSHAPE • CHECKPOINT • 3/10

## Slide 4
PROGRESS 2/4
Metric alignment is now board-anchored
R-23 removed the old camera-centre scale bias across all five golden objects.
R-23 GOLDEN-SET SCALE
s-01 board scale 0.9980 RMS 2.540 mm
s-02 board scale 0.9971 RMS 3.016 mm
s-03 board scale 0.9994 RMS 1.615 mm
s-04 board scale 0.9987 RMS 2.084 mm
s-05 board scale 0.9982 RMS 2.356 mm
Before
Legacy camera-centre scaling was roughly 0.907–0.958 on the golden set, making reconstructions visibly small.
After
Board-anchored scale is roughly 0.997–0.999. This gives provenance and future CAD inspection a defensible metric frame.
PROOFSHAPE • CHECKPOINT • 4/10

## Slide 5
PROGRESS 3/4
Provenance is becoming stricter—not more optimistic
R-24 and R-25 protect the hard rule: unseen geometry can never pass or fail a part.
R-24 CONFIDENCE FILTER
s-01 observations −3.1%
s-02 observations −4.0%
s-03 observations −4.5%
s-04 observations −4.2%
s-05 observations −2.8%
Only trusted reconstruction pixels may vouch for a vertex.
R-25 facing test
A vertex must now face the observing camera and agree with measured depth. Open-mesh normal direction uses only trusted, depth-consistent visible pairs.
Final coverage semantics
observed_fraction is computed after the sigma downgrade, weighted by triangle area, from the same final labels encoded in the GLB served to the user.
PROOFSHAPE • CHECKPOINT • 5/10

## Slide 6
PROGRESS 4/4
Generative AI supervises sampled capture frames
A-01 added real Gemini API checks without letting the model decide geometry.
What the VLM does
• Samples selected capture frames • Flags wrong-part / screen / obvious scene issues • Validates structured responses • Stores per-frame + aggregate evidence • Fails safely when unavailable
REAL API CHECK
30 JPEG golden frames available
11 valid Gemini replies recorded
screen / different-part controls checked
token usage recorded
evidence JSON persisted
Safety boundary
The VLM can contribute evidence and later veto an unsafe Pass, but it never computes metric geometry. Geometry, provenance and tolerances stay deterministic.
PROOFSHAPE • CHECKPOINT • 6/10

## Slide 7
TIMELINE
From capture prototype to inspection pipeline
Weeks 1–3
Capture + dataset
Phone permissions, guided capture, golden objects
Weeks 4–6
Reconstruction
VGGT, board pose, metric alignment, TSDF
Weeks 7–9
Evidence
Cleanup, provenance, uncertainty, endpoint
Weeks 10–11
Integration
Phone → real service, AI frame supervision
Weeks 12–13
Inspection
CAD registration, ICP, verdict/report close-out
PROOFSHAPE • CHECKPOINT • 7/10

## Slide 8
WHAT'S NEXT 1/2
Close R-25 with measured evidence—not assumptions
1 Golden rerun
Recompute R-23 board alignment, re-fuse once, then compare current-main vs R-25 on the exact same cleaned mesh for s-01…s-05.
2 Record the effect
Observed vertices, area-weighted final coverage, depth-gate rejection counts, sigma downgrades, and historical R-24 context.
3 Final close-out
Add measured hours, mark R-25 Done, run final CI, get teammate approval on the final head, then merge.
PROOFSHAPE • CHECKPOINT • 8/10

## Slide 9
WHAT'S NEXT 2/2
Move from reconstruction into CAD inspection
I-03 Global registration
Generate candidate CAD poses, keep metric scale fixed, and report free-scale residual as an integrity signal.
I-04 / I-05 Refine
Robust point-to-plane ICP with Tukey loss, then explicitly detect orientation ambiguity instead of hiding it.
End goal
Observed geometry → CAD deviation → Pass / Fail / Rescan / Unverifiable, with evidence that explains exactly why.
PROOFSHAPE • CHECKPOINT • 9/10

## Slide 10
REFERENCES
Project evidence used for this checkpoint
01
ProofShape GitHub repository — stories, decisions, tests, pull requests and CI
02
R-23 — board-anchored metric alignment golden-set evidence
03
R-24 — confidence-filtered provenance golden-set evidence
04
C-13 / PR #146 — real-phone → real-service integration evidence
05
A-01 / PR #207 — sampled Gemini VLM supervision evidence
06
R-25 / PR #213 — facing, sigma truncation and final observed coverage
07
ProofShape proposal, manual and frozen OpenAPI contract
Checkpoint deck • 10 slides • designed for a 5–7 minute presentation
PROOFSHAPE • CHECKPOINT • 10/10